## Slide 1
Exercises Session on Fault Detection
Federico Antonello
federico.antonello@polimi.it

## Slide 2: In this Exercise Session
Exercise 1
Homework 1
Method: AAKR
Component: Gas Turbine
Method: PCA
Component: Gas Turbine
Homework 2
Method: you choose
Component: Wind Turbine

## Slide 3
Exercise 1
Component: Gas Turbine

## Slide 4: Gas Turbine

## Slide 5: Measured Signals
Temperature location 1 (°C)
Temperature location 2 (°C)
Temperature location 3 (°C)
Temperature location 4 (°C)
Temperature location 5 (°C)
Temperature location 6 (°C)

## Slide 6: Available Data
Train.dat  Normal condition data [6 signals, 4000 data points, frequency: 5200 measuraments/year]
Temperature location 6 (°C)

## Slide 7: Available Data
Validation.dat  Normal condition data [6 signals, 2500 data points, frequency: 5200 measuraments/year]
Temperature location 6 (°C)

## Slide 8
Exercise 1
Method:AAKR

## Slide 9: Fault Detection using AAKR for signal reconstruction
COMPARISON
(-)
MODEL OF COMPONENT BEHAVIOR IN NORMAL CONDITIONS (AAKR)
DECISION
t
t
t
t
t
MEASURED SIGNALS
t
NORMAL
CONDITION:
No maintenance
ABNORMAL
CONDITION:
maintenance required
…
…
SIGNAL RECONSTRUCTIONS
RESIDUALS

## Slide 10: The AAKR code in Matlab: how to run the code?
Set as the current folder the folder ‘AAKR’
Run the code in the command window:
h: bandwidth parameter

## Slide 11: The AAKR code in Matlab: Output
6 figures (one for each signal) representing:
The original data and the reconstruction obtained using the AAKR algorithm
The residual for each data point
The reconstruction obtained using the AAKR algorithm
The Root Mean Square Error:

## Slide 12: The AAKR code in Matlab: Example
Execute the code in the command window:
Run the algorithm considering the bandwidth parameter h=0.1
5 minutes

## Slide 13
Exercise 1
Method: AAKR
Setting the model parameter:
h =bandwidth parameter
Objective: ACCURATE and ROBUST reconstruction model

## Slide 14: Accuracy
14
t
t
M
O
D
E
L
INPUT: NORMAL CONDITION DATA
t
t
Signal
reconstructions
Accurate reconstruction model if:
Metric to measure accuracy: Root Mean Square Error ():

## Slide 15: Accuracy – Results wit h=0.05 and h=0.4
Signal 6 normal condition
AAKR
h=0.05
h=0.4
h=0.05 results in a more accurate model

## Slide 16: Robustness
16
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Typically simulated)
M
O
D
E
L
Signal
reconstructions
Robust reconstruction if:

## Slide 17: Robustness
17
t
t
t
t
INPUT: ABNORMAL CONDITION DATA (Typically simulated)
M
O
D
E
L
OK
Signal
reconstructions
Robust reconstruction if:
Metric to measure Robustness:
Robustness
Reconstruction of the anomaly
Normal condition data (before anomaly simulation)

## Slide 18: Verify Robustness in Practice
Signal 6 normal condition
Signal 6 Abnormal condition
AAKR
Artificial simulated abnormal condition on signal 6
The other signals remain in normal condition
-- Signal 6 normal condition
-- Signal 6 abnormal condition
-- AAKR signal reconstruction
The method is robust if AAKK reconstruction is equal to the signal in normal condition

## Slide 19: Robustness – Results wit h=0.05 and h=0.4
Signal 6 normal condition
Signal 6 Abnormal condition
AAKR
-- Signal 6 normal condition
-- Signal 6 abnormal condition
-- AAKR signal reconstruction
Optimal value of h is a trade off between accuracy and robustness
h=0.05
h=0.4
More robust but less accurate
not robust but accurate

## Slide 20: Code to measure the method robustness
val = load('validation.dat’);
[npat,nsig]=size(val);
anomaly=load('validation_sim.dat’);
[test_reconstruction,rmse]=AAKR_reconstruction('train.dat','validation_sim.dat',0.05);
robustness=sum(((test_reconstruction(:,6)-val(:,6)).^2)/npat)^0.5

## Slide 21: Exercise 1A: Assignment
Set the bandwidth parameter () of the AAKR-based reconstruction model
You can use the following files:
Validation.dat  data in normal condition
Validation_sim.m data containing a simulated abnormal condition on signal 6
30-40 minutes

## Slide 22: Exercise 2
Perform the reconstruction of the signal measurements in the 4 files test_1.dat, test_2.dat, test_3.dat and test_4.dat.
In which files can you detect abnormal conditions? Do you have any hypothesis on the type of abnormal condition?
  Draw your conclusions on the possibility of using the developed model for fault detection.
30 minutes

## Slide 23
2. Analyze residuals with SPRT

## Slide 24: Exercise 3.0: Hints
Function  Computes the index value from the residuals of a test data and their reconstructions and stores them in the -by- vector .
INPUTS:
= -by- data matrix containing all patterns as rows and one signal in column of a test data
= -by-data matrix containing all reconstructed patterns as rows of one signal in column for the test patters of .
= False alarm rate
= Missed alarm rate.
= the mean of the Gaussian distribution of hypothesis (the component is working in normal conditions).
= variance of Gaussian distribution
= the mean of the Gaussian distribution of hypothesis (the component is working in abnormal conditions).
= variance of Gaussian distribution

## Slide 25: Exercise 3.1
Verify the capability of the SPRT method of detecting normal and abnormal conditions in evolution of signal 5 in “test_4A.dat” and “test_4B.dat” files. With respect to the parameters of the SPRT we suggest to use:
and Gaussian distributions for the two hypothesis and with parameters:
In which file do you detect the abnormal condition? When?
Compare the results with those of a threshold-based method with threshold = 1.
Draw your conclusions on the possibility of using the SPRT in decision-making for fault detection.

## Slide 26: Exercise 3.1: Hints
Function  Computes the index value from the residuals of a test data and their reconstructions and stores them in the -by- vector .
OUTPUTS:
= -by- vector of the values
EXAMPLE:

## Slide 27
Second Part

## Slide 28
Second Part
Fault detection with PCA considering turbine data
Optimize the PCA to achieve:
  a. Accuracy
  b. Robustness
Homework 1
3. Compare AAKR and PCA results
2. Analise tests data with the PCA model

## Slide 29: Plant Component Monitoring
S1
S5
S4
S3
S2
S6
Component
PCA
Reconstruction Model
S2
S5
S6
S3
S4
S1
S2
S5
S6
S3
S4
S1
Signal
Reconstructions
=
Expected signal values in normal conditions
Real
measurements

## Slide 30
PCA

## Slide 31: Fault Detection using PCA for signal reconstruction
COMPARISON
(-)
MODEL OF COMPONENT BEHAVIOR IN NORMAL CONDITIONS (PCA)
DECISION
t
t
t
t
t
MEASURED SIGNALS
t
NORMAL
CONDITION:
No maintenance
ABNORMAL
CONDITION:
maintenance required
…
…
SIGNAL RECONSTRUCTIONS
RESIDUALS

## Slide 32: How to use PCA algorithm in Matlab (1): Algorithm execution
Set as the current folder the folder:
‘PCA’
Execute the code in the command window:
v: variance

## Slide 33: How to use PCA algorithm in Matlab (2) Execution output
6 figures (one for each signal) representing:
The original data and the reconstruction obtained using the PCA algorithm
The residual for each data point
The reconstruction obtained using the PCA algorithm
The number of principal components corresponding to the selected variance
The RMSE

## Slide 34: Exercise 2:
Consider the patterns in file ‘train.dat’ to develop a PCA reconstruction model. The file contains data collected during normal conditions. They are 6 temperature signals, 5200 measuraments/year.
Develop the PCA reconstruction model
Perform the reconstruction of the file ‘validation.dat’. The file contains data collected during normal conditions
Hints:
Perform the computation considering different numbers of Principal Components
Consider the root mean square error as a performance measure. Two tests should be performed:
  Input = normal condition signals
  Input = simulated abnormal conditions
[test_reconstruction,n_PC, RMSE]=PCA_reconstruction(‘train.dat’,’validation.dat’,0.95)

## Slide 35
Second Part
Fault detection with Method you choose
Component: Wind Turbine
Homework 2

## Slide 36: The Monitoring System
Wind turbine farm built in 2002.
  Main Bearing+ Planetary Gear box + Gearbox + Generator

## Slide 37: The Monitoring System
  Monitoring system: 6 accelerometers and 1 sensor measuring the rotating speed
A10

## Slide 38: Failures Modes
  Crashing of the highspeed shaft of the gear box
  Breaking of a teeth in the planetary stage
  Misalignment between the generator and the gearbox shafts
  Wearing of the rear bearing housing of the generator

## Slide 39: Unplanned Maintenance
Gearbox-Generator Failure
    Three months of turbine downtime
    Intervention of expensive tools

## Slide 40: Current Diagnostic Protocol
  Data sent to the field operator and the diagnostic center
  Filed operator & expert in vibration signal analysis isolate anomalies.
    Expert knowledge required
    e.g. considering thresholds on vibration levels at different rotating speeds of the highspeed shaft
  Maintenance center assign a priority level (Green, Yellow, Red) for the intervention and plan the maintenance intervention

## Slide 41: Example
Wearing of the rear bearing housing of the generator
Vibration feature
Maintenance intervention

## Slide 42: Limitation of the Current Approach
Detection and Diagnosis Delays
Human errors
  Develop an “automatic” system for anomaly detection and diagnostic

## Slide 43: DESCRIPTION OF THE DATASET
A file contains 5 seconds of measurements of the accelerator at a frequency of 5.0kHz is collected each time at ‘Meas Time’ in the file.
Notes: The raw dataset are stored in 1019 ZA5.0kHz5s.csv 5.60 GB for A6; 4.84GB for A5

## Slide 44: Feature Extraction
…
Window 1
Feature
Window 2
Feature
Window 3
Feature
High frequency sensor:
10 k observations
10 k observations
10 k observations

## Slide 45: Feature Extraction
…
Window 1
Window 2
Window 3
Feature 1
Time t
Feature 2
Time t
…

## Slide 46: Feature Extraction
…
Window 1
Window 2
Window 3
Feature 1
Time t
Feature 2
Time t
PART 2 Fault Detection
Normal
Abnormal

## Slide 47: EXERCISE 1: FEATURE EXTRACTION
Each 5 sec signal data are divided in 40 segments(windows) in order to extract features
The following statistical features are considered:
Mean, standard deviation, Kurtosis, Skewnesss, min, max, 2nd moment, 3rd moment
A window contains values , the corresponding Statistical Features can be:
Sample Mean:
Sample Variance:
Standard Deviation:
-th Moments:
Kurtosis  “peak”
(the fourth standardized moment)
Skewness “asymmetry” (the third standardized moment)

## Slide 48: EXERCISE 1: FEATURE EXTRACTION
0
5

## Slide 49: EXERCISE 1 DEVELOPMENT OF A FAULT DETECTION TOOL FOR A WIND TURBINE GENERATOR
Given:
  The file ‘train.dat’ contains the features already extracted in norml condition
  The file ‘validation.dat’ contains the features already extracted in normal condition
  The file ‘validation_sim.dat’ contains the features in simulated abnormal condition
You are required to:
  Develop a fault detection tool for the turbine generator;
  Apply the developed tool to the data in the file “test.mat” Identify possible abnormal condition period.
Col 1 | Col 2 | Col 3 | Col 4 | Col 5 | Col 6 | Col 7 | Col 8
mean | std | kurtosiss | skewness | min | max | 2nd Moment | 3rd Moment

## Slide 50
  Homework 1
  Fault detection with PCA
Optimize the PCA to achieve Accuracy and Robustness
Analyze test data
  Homework 2
  Fault detection with AAKR on new data
Use data and code in foldier ‘PCA’
Use data and code in foldier ‘second case study’